2-bit adder Datasheet
***********************************************************************************
Clock frequency = 2GHz
Clock period = 500ps
***********************************************************************************
Area = 176.92992 um2
Length = 13.652 um
Width = 12.96 um
***********************************************************************************
Core Utilization = 95%
***********************************************************************************
Truth Table for 2 bit adder
***********************************************************************************
Top 3 Best case slack timing: 132.4ps, 93.7ps, 93.7ps
Top 3 Worst case slack timing: 24.6ps, 33.4ps, 34.6ps
***********************************************************************************
Power

Power Units = 1mW

Time Units = 1e-12 secs
-----------------------------------------------------------------------------------------
Total Power
-----------------------------------------------------------------------------------------
Total Internal Power: 0.02670523	68.6455%
Total Switching Power: 0.01218265	31.3153%
Total Leakage Power: 0.00001525	0.0392%
Total Power: 0.03890312
-----------------------------------------------------------------------------------------

Group	Internal Switching Leakage Total Percentage
        Power Power Power Power (%)
-------------------------------------------------------------------------------------------------------------------
Sequential	0.009628 0.0007958 3.644e-06 0.01043 26.8
Macro	0 0 0 0 0
IO	0 0 0 0 0
Combinational	0.01708 0.01139 1.16e-05 0.02848 73.2
Clock (Combinational) 0 0 0 0 0
Clock (Sequential) 0 0 0 0 0
-------------------------------------------------------------------------------------------------------------------
Total	0.02671 0.01218 1.525e-05 0.0389 100
---------------------------------------------------------------------------------------------------------------------
Rail Voltage Internal Switching Leakage Total Percentage
        Power Power Power Power (%)
------------------------------------------------------------------------------------------------------------------------
vdd 0.7 0.02671 0.01218 1.525e-05 0.0389 100

Power Distribution Summary:
Highest Average Power: g191 (INVx13_ASAP7_75t_R):	0.005504
Highest Leakage Power: FE_OFC4_n_14 (BUFx12f_ASAP7_75t_R):	7.991e-07

***********************************************************************************
Total capacitance: 9.7032 e-14 F
***********************************************************************************
Schematic View: